## Slide 1: High performance computing in computational fluid dynamics

## Slide 2: Hierarchy of computational aerodynamics approaches:

## Slide 3
Engineering methods (or semi-empirical methods) combine theory and experimental data.

## Slide 4
Linear Potential Flow Methods: are based on the potential flow assumptions.
Linear Potential Flow Methods are valuable for performing conceptual or preliminary design, since they are relatively fast on modern computers.

## Slide 5
CFD methods: are the “highest” level of simulation possible.
CFD methods solve the governing equations of fluid dynamics using numerical methods.
They often require some of the fastest, largest computer systems available referred to as high-performance computing.
CFD methods have been reserved for determining details about a flow-field.
CFD prediction of Hyper-X flowfield at M=7 with engine operating (Courtesy of NASA Dryden Flight Research Center).

## Slide 6: When should we use a given method ?!
Given the choices shown previously in the table, it is not always easy to know which approach to use at any given time.
This type of engineering judgement is usually based on experience, not just knowledge of the various approaches.
A common sense approach we can follow is: “don’t use cannons to shoot flies and don’t shoot spit wads at battleships”
So we use the method that is best suited for the results and purposes of our investigation.

## Slide 7: nAVier-stokes equations:

## Slide 8: Why cfd requires large computers:
Reynolds-Averaged Navier-Stokes equation:
If we are solving the 3-D RANS equation, we are calculating the following flow parameters: density, velocity (3 components), pressure, temperature, and viscosity.
In addition to that, we will require the (x,y,z) position of each grid point.
So we need to keep track of at least 10 variables at each gridpoint.
The following figure shows the surface grid points on the Space Shuttle Orbiter. Every intersection of lines on the surfaces represents a location where all the flow variables are computed.

## Slide 9
A 3-D grid in this case can easily consist of 10 million grid points.
So we need to know 10 values at 10 million grid points, or, in other words, at any moment during the solution process we have to keep track of 100 million pieces of information.
We will need to use a numerical algorithm to find the solution !

## Slide 10
This will require thousands of operations on these 100 million pieces of information.
How long will it take?
What if it takes 6 months?
Will we remember the question we were asking if we wait six months to find out the answer?
I personally doubt it !
Fortunately for people who work in CFD, computer processing speeds, memory, and storage have been increasing rapidly.
CFD is directly linked to the advancement of computers.

## Slide 11: Performance of a cfd code on a parallel computer
Megaflop vs number of processors
Efficiency of a specific code:
Speedup:
Cost:

## Slide 12: Parallel computing scalability
Scalability: how does the efficiency of the computation depend on the number of processors?
Ideal case is a linear behavior: code runs n times on n number of processors.
Amdahl’s Law: maximum speedup that can be achieved =
F: fraction of a calculation that is sequential (can not benefit from parallelization)
(1-F): fraction that can be parallelized

## Slide 13: The main challenges of cfd:
Physical Models:
1- Need to gain a greater understanding of turbulence and its effect on transfer of heat, mass, and momentum.
2- Complex geometry of flow domain in most problems of industrial applications.
Computational Requirements:
1- Faster processors and larger memories
2- “Intelligent” software algorithms

## Slide 14: Examples of HPC Successes and challenges:
Example of HPC Success: Boeing 787 Dreamliner
11 prototype wing designs vs 77 for the Boeing 777
Example of HPC challenges: Modelling of a Scramjet Engine
1- Trade-offs needed which yield errors
2- Full simulations required to model the complete physics may need computers 100 to 1000 times larger than the ones available.
3- Computations were conducted on 163,000 processors simultaneously.

## Slide 15: The art of cfd: